## Slide 1
Utilizing GIS to Improve
Regional Water Planning
Shellby Miller & Ansley Murphy
Metropolitan North Georgia Water Planning District
Stormwater Forecast & River Basin Profiles

## Slide 2: Metropolitan North Georgia Water Planning District
15 Counties
96 Cities
99% of our drinking water is supplied through Surface Water Sources

## Slide 3: Created by the Georgia Legislature in 2001
Metro Water District
develops regional Water Resources Management Plan
Local governments responsible for implementing plans
Georgia EPD approves plans and enforces implementation via permits and state funding eligibility

## Slide 4
Metro Atlanta’s Rainfall is Changing
Average Annual Rainfall = 50 inches
Annual Rainfall

## Slide 6: Current stormwater metrics
Municipal Separate Storm Sewer System Compliance (MS4)
303(d)/ 305(b) List of Impairment
Land Use Plans Reviewed
Stormwater Projects Completed
Citizen Complaints
  Flooding
  Sinkholes
  Stream Bank Erosion
https://wefstormwaterinstitute.org/programs/ms4survey/

## Slide 7
Goals for a New Approach
Identify a metric that facilitates new conversations in stormwater management
Shift the stormwater paradigm from activity and compliance-based management to performance and function-based management
Evaluate existing and future watershed conditions through 2040
  Future development
  Future meteorological trends

## Slide 8: Stormwater Forecast Overview
Planning-level estimate of the total potential runoff management volume from development
Calculated at a Basin Scale
Four Planning Scenarios
  Predevelopment, 2019, 2030, & 2040
Using three Post-Construction SW Management Standards
  Water Quality Volume (WQv)
  Channel Protection Volume (CPv)
  Overbank Flood Protection Volume (OFPv)
2019 WQv

## Slide 9: Stormwater Forecast Calculations
Input Data
County, HUC-12, & NHD Subcatchment Boundaries
USGS 1/3 Arcsec DEM
USGS NLCD – 2001 & 2019
NRCS SSURGO (Soils)
NOAA Atlas 14 Rainfall
USGS Future Urbanization – through 2040*
Future Rainfall Depths – through 2040
Rainfall Depths
Drainage Area
Basin Slope
Land Cover
Imperviousness
Hydrologic Soil Groups
Time of Concentration
Direct Runoff
Initial Abstraction
Curve Number
Peak Discharge
Water Quality
Channel Protection
Overbank Flood Protection
Runoff Volume Results
Watershed Characteristic
USGS Southern Megalopolis Study: https://doi.org/10.1371/journal.pone.0102261

## Slide 10: Stormwater Forecast as a New Metric
Total Potential Runoff Volume
Runoff
Currently Managed
?
New Metric for Stormwater Program Management
Gap to manage
New Home Price
Current Savings
Amount needed for the new home

## Slide 11
District-wide Stormwater Forecast Information
Chart: Rainfall (inches)
| 85th Percentile Annual Rainfall (WQv) | 1-Year, 24-Hour Rainfall (CPv) | 25-Year, 24 Hour Rainfall (OFPv)
2019 | 1.2 | 3.34 | 6.12
2030 | 1.32 | 3.59 | 6.76
2040 | 1.37 | 3.71 | 7.1
Current And Future District-wide Rainfall Depths by Design Storm
16% Increase from 2019
14% Increase from 2019
11% Increase from 2019

## Slide 12: Stormwater Management Volumes are Increasing
116% - Water Quality Volume
89% - Channel Protection Volume
103% - Overbank Flood Protection Volume
Percent change: 2019 to 2040
2019
2040
Overbank Flood Protection Volume

## Slide 13
Want to know more?
District Website: northgeorgiawater.org
Select: Plans & Reports

## Slide 14
What’s Next?
Publish to ARC Data Hub
Develop Snapshot tool using ArcGIS API for JavaScript and React

## Slide 15
https://arcg.is/1DjqWn

## Slide 16: Thank you
Shellby Miller, Senior Data & GIS Analyst
smiller@atlantaregional.org
Ansley Murphy, GIS Intern
amurphy@atlantaregional.org